## Slide 1: UNIT V
ROM

## Slide 2: ROM
Read‐only memory (ROM)
  Permanent binary information
  The binary information specified by the designer
  Static and Non volatile

## Slide 3: Types of ROM
Programmed in different ways
Mask programming
PROM
    Programmable read‐only memory
EPROM
    Erasable PROM
EEPROM
    Electrically erasable PROM (EEPROM or E2PROM)
Flash memory devices

## Slide 4: Types of ROM
1. Mask programming
  Programming is done by the semiconductor company
  During the last fabrication process of the unit
  Customer fill out the truth table
  In a special form provided by the manufacturer
  The manufacturer makes the corresponding mask for the paths to produce the 1’s and 0’s according to the customer’s truth table
  Costly because the vendor charges
  Economical only if a large quantity of the same configuration

## Slide 5: Types of ROM
2. PROM
Programmable read‐only memory
    Fuse
    Initially all the fuses are intact ie: all bits are 1
    Fuses are blown by the application of a high‐voltage pulse to the device through a special pin
    A blown fuse defines a binary 0 state and an intact fuse gives a binary 1 state
    This procedure allows the user to program
    Special instruments called PROM programmers are available commercially to facilitate the procedure
    Procedures for programming ROMs are hardware procedures, even though the word
    programming is used
    Once programmed then irreversible

## Slide 6: Types of ROM
3. EPROM
Erasable PROM
    Can be restructured to the initial state even though it has been programmed previously
    When placed under a special ultraviolet light for a given length of time, the shortwave radiation discharges the internal floating gates that serve as the programmed connections
    Can be reprogrammed to a new set of values

## Slide 7: Types of ROM
4. EEPROM
Electrically erasable PROM (EEPROM or E2PROM)
    Like EPROM
    Except that the previously programmed connections can be erased with an electrical signal instead of ultraviolet light
    The advantage is that the device can be erased without removing it from its socket

## Slide 8: Types of ROM
5. Flash memory devices
  Similar to EEPROMs
  But have additional built‐in circuitry to selectively program and erase the device in‐circuit, without the need for a special programmer
  Application in modern technology
  Cell phones, digital cameras, set‐top boxes, digital TV, telecommunications, nonvolatile data storage, microcontrollers
  Their low consumption of power makes them an attractive storage medium for laptop and notebook computers

## Slide 9: ROM
32 * 8 ROM
32 words of 8 bit each
5 bits represent 32 different address
5*32 decoder is used
Decoder need 32 AND gates with 5 input each
Output need 8 OR gates with 32 input each
32*8 = 256 intersections
Decoder
32*8 Rom

## Slide 10: ROM
32*8 Rom
32*8 ROM
  32 AND gates
  8 OR gates
  In general
2k*n ROM
  2K AND gates
  n OR gates

## Slide 11: Programmable logic device (PLD)
Programmable logic device (PLD)
    Electronic component used to build digital circuits
    It must be programmed before using in a circuit
    The binary information in a specified fashion is stored and then embedded within the hardware in a process is referred to as programming the device
  Examples of PLDs:
    PROM
    Programmable logic array(PLA)
    Programmable array logic (PAL)
    Field‐programmable gate array (FPGA)

## Slide 12: Basic configuration of three PLDs

## Slide 13: PROM
256 intersections are programmable
Intersections are equivalent to a switch
Called - crosspoint
Various physical devices are used to implement crosspoint switches
Simplest technologies – fuse
Fuse is opened or “blown” by the application of a high‐voltage pulse

## Slide 14: PROM
Fuse is opened or “blown” by the application of a high‐voltage pulse
Fuse blown for ‘0’
Other wise it is ‘1’
Eg address 3
  Data 10110010
  Blown A6,A3,A2,A0

## Slide 15: Combinational Circuit Implementation
Truth table specifies the content in each address word

## Slide 16: Combinational Circuit Implementation : example
Design a combinational circuit using a ROM. The circuit accepts a three‐bit number and
outputs a binary number equal to the square of the input number.

## Slide 17: Combinational Circuit Implementation : example

## Slide 18: PROGRAMMABLE LOGIC ARRAY
Similar to the PROM
Except that the PLA does not provide full decoding of the variables
Also it does not generate all the minterms
The decoder is replaced by an array of AND gates
And gates can be programmed to generate any product term of the input variables
The product terms are then connected to OR gates to provide the sum of products for the required Boolean functions

## Slide 19: PROGRAMMABLE LOGIC ARRAY
X xor 1= X’
X xor 0 = X

## Slide 20: PROGRAMMABLE LOGIC ARRAY
Path between i/p and AND gate
Path between AND gate and OR gate
T : True
C : Complement
1 : True
0 : Complement
- : Term is absent

## Slide 21: PROGRAMMABLE LOGIC ARRAY
X xor 1= X’
X xor 0 = X

## Slide 22: PROGRAMMABLE LOGIC ARRAY
To design PLA
  n input
  k product term
  m output
Needs
  n buffer- inverter gates
  k AND gates
  m OR gates and XOR gates
Eg: 3 input 4 product term 2 output

## Slide 23: PLA : example
  Implement the following two Boolean functions with a PLA:

## Slide 24: PLA : example
A/BC | 00 | 01 | 11 | 10
0 | 1 | 1 |  | 1
1 | 1 |  |  | 
A/BC | 00 | 01 | 11 | 10
0 | 1 |  |  | 
1 |  | 1 | 1 | 1
A/BC | 00 | 01 | 11 | 10
0 |  |  | 0 | 
1 |  | 0 | 0 | 0
A/BC | 00 | 01 | 11 | 10
0 |  | 0 | 0 | 0
1 | 0 |  |  | 
F1=A’B’+A’C’+B’C’
F1’=BC +AB +AC
F2=A’B’C’ + AB +AC
F2’ = ABC +A’B +A’C
F1’ and F2 has many terms in common

## Slide 25: PLA : example
F1’=BC +AB +AC
F2=A’B’C’ + AB +AC
F1’ and F2 has many terms in common
 | Product Term | Input A B C | Output (T) F1 F2
AB | 1 | 1 1 - | 1
AC | 2 | 1 - 1 | 1
BC | 3 | - 1 1 | 1 -
A’B’C’ | 4 | 0 0 0 | - 1

## Slide 26: PLA : example
F1’=BC +AB +AC
F2=A’B’C’ + AB +AC
F1’ and F2 has many terms in common
 | Product Term | Input A B C | Output (T) F1 F2
AB | 1 | 1 1 - | 1
AC | 2 | 1 - 1 | 1
BC | 3 | - 1 1 | 1 -
A’B’C’ | 4 | 0 0 0 | - 1
F2
F1
1
0
FPGA
C C’ B B’ A, A’
0

## Slide 27: PLA : example
F1’=BC +AB +AC
F2=A’B’C’ + AB +AC
F1’ and F2 has many terms in common
 | Product Term | Input A B C | Output (T) F1 F2
AB | 1 | 1 1 - | 1
AC | 2 | 1 - 1 | 1
BC | 3 | - 1 1 | 1 -
A’B’C’ | 4 | 0 0 0 | - 1
F2
F1
1
0
FPGA
C C’ B B’ A, A’
0

## Slide 28: PAL
PLD with fixed OR array and a programmable AND array
Is easier to program
But is not as flexible as, the PLA.
Figure AND–OR array that is three wide, the term used to indicate that there are three programmable AND gates in each section and one fixed OR gate

## Slide 29: PAL

## Slide 30: PAL : Boolean Function example

## Slide 31: PAL : Boolean Function example
AB/CD | 00 | 01 | 11 | 10
00 |  |  |  | 1
01 |  |  |  | 
11 | 1 | 1 |  | 
10 |  |  |  | 
AB/CD | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  |  | 1 | 
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 1 | 1
AB/CD | 00 | 01 | 11 | 10
00 | 1 |  | 1 | 1
01 | 1 | 1 | 1 | 1
11 |  |  | 1 | 
10 | 1 |  | 1 | 1
AB/CD | 00 | 01 | 11 | 10
00 |  | 1 |  | 1
01 |  |  |  | 
11 | 1 | 1 |  | 
10 | 1 |  |  | 

## Slide 32: PAL : Boolean Function example

## Slide 33: SEQUENTIAL PROGRAMMABLE DEVICES
Digital systems are designed with flip‐flops and gates.
Combinational PLD consists of only gates
It is necessary to include external flip‐flops to PLD
Sequential programmable devices include both gates and flip‐flops
It can be programmed to perform a variety of sequential‐circuit functions
Three major types
1. Sequential (or simple) programmable logic device (SPLD)
2. Complex programmable logic device (CPLD)
3. Field‐programmable gate array (FPGA)

## Slide 34: SPLD
Sequential (Simple) PLD
IC includes
Flip‐flops
AND–OR array
A PAL or PLA include flip‐flops to form a register
Outputs can be taken from the OR gates or from flip‐flops
D or JK Flip flop is used

## Slide 35: SPLD
PLA
Field‐programmable logic sequencer (FPLS)
The first programmable device to support sequential circuit implementation
FPLS is organized around a PLA with several outputs driving flip‐flops
The flip‐flops are flexible - programmed to operate as either the JK or the D
Disadvantage
Did not succeed commercially
Due to too many programmable connections
PAL
A PAL that includes flip‐flops is referred to as a registered PAL
To signify that the device contains flip‐flops in addition to the AND–OR array

## Slide 36: SPLD
SPLD is called a macrocell
Circuit that contains a SOP combinational logic function and an optional flip‐flop
AND–OR sum‐of‐products function or it can be any one of the two‐level implementations
Typical SPLD has from 8 to 10 macrocells within one IC package

## Slide 37: SPLD
Basic macrocell logic

## Slide 38: CPLD
The design of a digital system often requires the connection of several PLD devices to produce the complete specification
It is more economical to use a CPLD
It is a collection of individual PLDs on a single integrated circuit
A programmable interconnection structure allows the PLDs to be connected to each other

## Slide 39: CPLD
The device consists of multiple PLDs interconnected through a programmable switch matrix
The input–output (I/O) blocks provide the connections to the IC pins
Each I/O pin is driven by a three state buffer and can be programmed to act as input or output
The switch matrix receives inputs from the I/O block and directs them to the individual macrocells
Selected outputs from macrocells are sent to the outputs as needed
Each PLD typically contains from 8 to 16 macrocells
If a macrocell has unused product terms, they can be used by other nearby macrocells.
Macrocell flip‐flop is programmed to act as a D, JK, or T flip‐flop

## Slide 40: CPLD

## Slide 41: FPGA
A field‐programmable gate array (FPGA) is a VLSI circuit that can be programmed at the user’s location
It is an array of millions of logic blocks surrounded by programmable input and output blocks and connected together via programmable interconnections
There is a wide variety of internal configurations
The performance of each type of device depends on the circuit contained in its logic blocks and the efficiency of its programmed interconnections
A typical FPGA logic block consists of lookup tables, multiplexers, gates, and flip‐flops

## Slide 42: FPGA
A lookup table is a truth table stored in an SRAM and provides the combinational circuit functions for the logic block
The combinational logic section, along with a number of programmable multiplexers, is used to configure the input equations for the flip‐flop and the output of the logic Block
The advantage of using RAM instead of ROM to store the truth table is that the table can be programmed by writing into memory
The disadvantage is that the memory is volatile and presents the need for the lookup table’s content to be reloaded in the event that power is disrupted
The program can be downloaded either from a host computer or from an onboard PROM.
The program remains in SRAM until the FPGA is reprogrammed or the power is turned off
The device must be reprogrammed every time power is turned on
The ability to reprogram the FPGA can serve a variety of applications by using different logic implementations in the program